AIA/SDO FITS Keywords for Scientific Usage and Data Processing at Levels 0, 0.1, 0.3, 0.5, 0.8, and 0.9

(A document in progress)

Keyword Nomenclature:

(Telemetry keywords are bold italic; derived keywords are bold; & potential keywords are italic)

{#  = Integer (~ 0-999); @ = Optional single character A-Z; & = Alpha-numeric}

LL@#         		Lower Left corner pixel for row (X) / column (Y) for Region of Interest

(ROI) # on CCD

NAXIS@#                   Dimension (in pixels) along row (X) / column (Y) for ROI # on CCD

A@&&&&&&	Originating from telemetry data (@: H = HDR, F = FDB, I = ISP)

(Note: The definitions of the output data levels included below have been extracted in part from the Stanford SDO DRMS and SUMS computer database, as well as from Phil Scherrer’s JSOC Keywords Notes and Processing Plan for Level-0.)

1. Basic Image Information for Level-0 (and Above)

Definition of Level-0

1.  Image Header

Generated from metadata, it consists only of keywords derived directly from the image camera header data and those stored in a ground database containing the image characteristics, such as image size, date of observation, telescope, instrument, etc.

2.  Image Data

Decompressed raw data recompressed using gzip (see http://www.gzip.org/).

From science data packet image header (HDR) information (definition in Doc. AIA02019):

AHAPID = Packet APID (11b; from HDR)

AHTCS   = Time Code Seconds (32b; from HDR)

AHTCSS = Time Code Sub Seconds (32b; from HDR)

AHTLFSN = Camera/Frame Serial Number (32b; from HDR)

AHT1RN   = Target 1 Row Number (7b; from HDR) for the lower-left pixel of ROI1 (to

the nearest 32nd row or column)

AHT1CN   = Target 1 Column Number (7b; from HDR) for the lower-left pixel of ROI1

AHT2RN   = Target 2 Row Number (7b; from HDR) for the lower-left pixel of ROI2

AHT2CN   = Target 2 Column Number (7b; from HDR) for the lower-left pixel of ROI2

AHFDBID = Frame Definition Block ID (8b; from HDR)

AHTAPC = TAP Code (4b; from HDR)

AHBITID = Bit Select ID (4b; from HDR)

AHCPIDN = Compression parameter n (4b; from HDR)

AHCPIDK = Compression parameter k (4b; from HDR)

AHLUTID = Lookup Table ID (8b; from HDR)

The 2 highest order bits in the 32b Frame Serial Number field will be used to specify the AIA camera (telescope) number,  CAMERA , associated with the data image, such that

AHTLFSN   = AHTELID (2b; telescope # -1) + AHFSN [Frame Serial Number (the least significant 30b)], where

AHTELID = [0, 1, 2, 3] = CAMERA – 1, or    CAMERA = AHTELID + 1 = [1, 2, 3, 4].

From Frame Definition Block (FDB) (generated and stored in database on the ground [GDB]):

AFDBID = Frame Definition Block ID (8b; from GDB)

AFCRM = CCDReadoutMode (4b; from GDB) for number of ports: 1, 2, 4 (= 3, 2, 1)

AFDBSM   = SummingMode (4b; from GDB) for summing: 1x1, 2x2, 4x4 (= 0, 1, 2)

AFDBNW  = NumWindows (4b; from GDB) for number of ROI windows (= 0, 1, 2)

AFNR1 = NumRows1 (16b; from GDB) for height of region 1 in pixels

AFNC1 = NumCols1 (16b; from GDB) for width of region 1 in pixels

AFNR2 = NumRows2 (16b; from GDB) for height of region 2 in pixels

AFNC2 = NumCols2 (16b; from GDB) for width of region 2 in pixels

AFDBRL = RowLength (16b; from GDB) for row length in pixels for all extracted regions

Using the basic keywords above for the lower-left pixel of the 2 target regions of interest (ROI) and for the widths and heights of the regions, together with the following figure from the AIA Sequence Control Document (#AIA02019), where the lower-left corner pixel (LLC) is the origin with columns designated along the horizontal axis and rows along the vertical axis, the derived keywords below can be determined for each of the ROIs, 1, 2, and ROI 3 in between, if the first two ROIs are overlapping in rows but not columns, as shown. It is assumed in the ROI figure below that nominal solar north direction is at the top of the figure. (This will be validated, or rotations will be made so solar north is up, in Level-0.3 when the ancillary data for instrument pointing and spacecraft pointing, roll, location, and velocity become available.)

LLC

Derived Keywords:

NUMWIN = AFDBNW  + TBD      [number of window ROIs:

= 0 for full (4kx4k) CCD (TBD = 0);

= 1 for 1 ROI (TBD = 0);

= 2 for 2 ROI (TBD = 0);

= 3 for extra region when first 2 regions have overlapping

rows but not columns (TBD = 1), as in the figure.]

LLX1 = AHT1CN * 32                     [region 1 (R1) at center of lower left corner pixel, X variable]

LLY1 = AHT1RN * 32	           [R1 at center of lower left corner pixel, Y variable]

LLX2 = AHT2CN * 32 	           [R2 at center of lower left corner pixel, X variable]

LLY2 = AHT2RN * 32	           [R2 at center of lower left corner pixel, Y variable]

LLX3 = LLX1 + AFNC1                  	[gray region (R3) at center of lower left corner, X variable]

LLY3 = LLY1			[R3 at center of lower left corner, Y variable]

NAXISX1 = AFNC1		          	[R1 number of pixels along X axis]

NAXISY1 = AFNR1		           	[R1 number of pixels along Y axis]

NAXISX2 = AFNC2		         	[R2 number of pixels along X axis]

NAXISY2 = AFNR2		          	[R2 number of pixels along Y axis]

NAXISX3 = AFDBRL – AFNC1 – AFNC2  [R3 number of pixels along X axis]

NAXISY3 = LLY2 + AFNR2 – LLY1	  [R3 number of pixels along Y axis]

NAXIS = 2, 2, 1, 1                             [corresponds to number of axes of images for NUMWIN = 0,

1, 2, 3, respectively, to not confuse simple FITS  file readers.]

NAXIS1 = 4096, NAXISX1, total number of pixels in area, total number of pixels in area

NAXIS2 = 4096, NAXISX2, 0, 0

[the first 2 values of NAXIS# correspond, respectively, to the axis length for  NUMWIN = 0, 1 and the last 2 values correspond to the total number of pixels in ROIs for NAXIS1 and to zero by definition for NAXIS2 to not confuse simple FITS  file readers for NUMWIN = 2, 3.]

(TBD if any ROI frames will be directly viewable without further processing at Level-0.1.)

Quality/Sanity Check of FDB ID:

Does AHFDBID = AFDBID ?

Reconstructing the acquired image requires, in addition, the appropriate use of AHCPIDN, AHCPIDK, AHTAPC, AHBITID, AHLUTID, AFDBSM, and AFCRM. The observation time can be determined (TBD) from AHTCS and AHTCSS.

----------

TELESCOP = “SDO/AIA”	text, Name of source telescope package

INSTRUME = “AIA_i”	text, Name of instrument (within telescope package) where i =

camera number = 1, 2, 3, or 4

SIMPLE = “T”	         	Boolean, always T for True, if conforming FITS file

BITPIX = “16” (?)	         	integer, Bits/pixel: 16, 32, -32, or -64 (negative for floating point)

(HMI uses as 16 in L0)

DATE				text, Date and time of file creation in format:

yyyy.mm.ddThh:mm:ss[.sss]

in UTC as text

DATE-OBS			Date and time when observation of this image started (uses DATE

format)

MJD				float, Date of observation as modified julian day

TIME				float, Time of observation in seconds within a day. MJD and TIME

describe the same instant as DATE-OBS

ORIGIN			text, Location where file was made, e.g., “SDO/JSOC-SDP”

2.  Additional Information for Level-0.1 (and Above)

Definition of Level-0.1      (Note: The intended use of this level is for JSOC-OPS quick-look viewing in near-real time.)

1.  Image Header

Metadata for Level-0 plus that generated from the associated image status packet (ISP), including the status of every mechanism, the camera itself, the image stabilization system (ISS), and the guide telescope (GT). (See latest image status packet list)

2.  Image Data

Decompressed raw data recompressed using gzip. (Same as that for Level-0)

(Note: At Level-0.1 there will be a different series of header and image data for each camera (telescope) and possibly three series for ROIs, differentiated by the number of ROI.)

More Basic Keywords for ROI Quality/Sanity Check:

AICRS = A838F = AIA_IMG_CCD_ROW_START (16b; from ISP) in pixels

AICRE = A8390 = AIA_IMG_CCD_ROW_END (16b; from ISP) in pixels

AIR1CS = A8396 = AIA_IMG_ROI_1_COL_START (16b; from ISP) in pixels

AIR1CE = A839A = AIA_IMG_ROI_1_COL_END (16b; from ISP) in pixels

AIR2CS = A8397 = AIA_IMG_ROI_2_COL_START (16b; from ISP) in pixels

AIR2CE = A839B = AIA_IMG_ROI_2_COL_END (16b; from ISP) in pixels

ROI Quality/Sanity Check (using ISP & FDB keywords to obtain the same derived keywords as above):

LLX1 = AICRS					[R1 lower left corner, X variable]

LLY1 = AIR1CS					[R1 lower left corner, Y variable]

LLX2 = AICRE – AFNC2				[R2 lower left corner, X variable]

LLY2 = AIR2CS					[R2 lower left corner, Y variable]

LLX3 = LLX1 + AFNC1 				[R3 lower left corner, Y variable]

LLY3 = LLY1 					[R3 lower left corner, Y variable]

NAXISX1 = AFNC1					[R1 number of pixels along X axis]

NAXISY1 = AIR1CE – LLY1   			[R1 number of pixels along Y axis]

NAXISX2 = AFNC2					[R2 number of pixels along X axis]

NAXISY2 = AIR2CE – LLY2   			[R2 number of pixels along Y axis]

NAXISX3 = LLX2 – LLX1 – AFNC1		[R3 number of pixels along X axis]

NAXISY3 = AIR2CE – LLY1  			[R3 number of pixels along Y axis]

AICNTC = A8317 = AIA_IMG_CENTER_COL (16b; from ISP)

AICNTR = A8316 = AIA_IMG_CENTER_ROW (16b; from ISP)

AICSFT = A8319 = AIA_IMG_COL_SHIFT (16b; from ISP)

AIRSFT = A8318 = AIA_IMG_ROW_SHIFT (16b; from ISP)

CCD Information

AIPSM = A838B = AIA_IMG_PAR_SUM_MODE (8b; from ISP)

AISSM = A8388 = AIA_IMG_SER_SUM_MODE (8b; from ISP)

Quality/Sanity Check with FDB Summing Mode (TBD)

2.1 Instrument, Mechanisms, & Observable Information

AISTATE = A8284 = AIA_IMG_STATE (3b; from ISP)

from which the camera (telescope) number, CAMERA, can be sanity checked and the ISS

status bit on,  ISS, can be obtained.

AITELID = AIA_IMG_TELESCOPE_ID (2b; from ISP)

from which again the camera (telescope) number, CAMERA, can be sanity checked.

AIMGFSN = AIA_IMG_FSN (30b; from ISP)

from which frame serial number can be sanity checked.

AIASEN = A82BF = AIA_IMG_AS_ENCODER (16b; from ISP)

AIFWEN = A8292 = AIA_IMG_FW_ENCODER (8b; from ISP)

WAVELNTH = AIA_IMG_WAVELENGTH (8b; from ISP),    wavelength of observation:

2 each for telescopes 1, 2, 4 and 4 for telescope 3 (as a float in nm (Phil))

AIFILTYP = AIA_IMG_FILTER_TYPE (1b; from ISP)

AIMGTYP = AIA_IMG_IMAGE_TYPE (8b; from ISP),  	     dark/light/cal, “shutter type”

AIDCOFST = AIA_IMG_DC_OFFSET (16b; from ISP)

AIIOFSTY = AIA_IMG_ISS_OFFSET_Y (16b; from ISP)

AIIOFSTZ = AIA_IMG_ISS_OFFSET_Z (16b; from ISP)

AIGTSIGV = AIA_IMG_GT_SIGNAL_VAL (16b; from ISP)

AIAECTI = A82CA = AIA_IMG_AEC_TABLE_ID (16b; from ISP)

AIAECENF = AIA_IMG_AEC_ENA_FLAG (1b; from ISP)

AIAECTYP = AIA_IMG_AEC_TYPE (2b; from ISP),     		“target type”

AIAECSUP = AIA_IMG_AEC_STEPUP (16b; from ISP)

AIAECSDN = AIA_IMG_AEC_STEPDN (16b; from ISP)

AIFOENFL = AIA_IMG_FOCUS_ENA_FLAG (1b; from ISP)

AIFTSWTH = AIA_IMG_FLT_TYP_SW_TH (16b; from ISP),  	filter switch threshold

Exposure Information:

AIMGSHEN = A8296 = AIA_IMG_SH_ENCODER (8b; from ISP)

AIMGOTS = A8285 = AIA_IMG_OBT_TIME_SH_SEC (32b; from ISP)

AIMGOTSS = A8286 = AIA_IMG_OBT_TIME_SH_SS (16b; from ISP)

AIMGSHCE = A8213 = AIA_IMG_SH_CMDED_EXPOSURE (16b; from ISP)

AIMSHOBC = A853E = AIA_IMG_SH_OPEN_BOT_CENTR (24b; from ISP)

AIMSHOBE = A853F = AIA_IMG_SH_OPEN_BOT_EDGE (24b; from ISP)

AIMSHOTC = A8540 = AIA_IMG_SH_OPEN_TOP_CENTR (24b; from ISP)

AIMSHOTE = A8541 = AIA_IMG_SH_OPEN_TOP_EDGE (24b; from ISP)

AIMSHCBC = A8214 = AIA_IMG_SH_CLOSE_BOT_CENTR (24b; from ISP)

AIMSHCBE = A8291 = AIA_IMG_SH_CLOSE_BOT_EDGE (24b; from ISP)

AIMSHCTC = A853C = AIA_IMG_SH_CLOSE_TOP_CENTR (24b; from ISP)

AIMSHCTE = A853D = AIA_IMG_SH_CLOSE_TOP_EDGE (24b; from ISP)

-------------

EXPTIME			Exposure time in seconds

2.2 Time Information

ATCSO27 = APID027_TIMECODE_SECONDS (32b; from ISP)

ATCSS027 = APID027_TIMECODE_SUBSECS (32b; from ISP)

Another Quality/Sanity Check can be performed for the observation time

Sequence/State Information

ASQFGSN = AIA_SEQ_FRAME_SN (32b; from ISP)

ASQFGID = AIA_SEQ_FRAME_ID (32b; from ISP)

AIFCPS = A8225 = AIA_IMG_FC_POSITION (16b; from ISP)

AIFDBID = A8315 = AIA_IMG_FDB_ID (16b; from ISP)

AIFTSID = AIA_IMG_FTS_ID (16b; from ISP)

AIFRMLID = AIA_IMG_FRMLIST_ID (16b; from ISP)

AIEVENT = AIA_IMG_EVENT (8b; from ISP)

AICFGDL1 = AIA_IMG_CFG_DELAY_1 (8b; from ISP)

AICFGDL2 = AIA_IMG_CFG_DELAY_2 (8b; from ISP)

AICFGDL3 = AIA_IMG_CFG_DELAY_3 (8b; from ISP)

AICDGDL4 = AIA_IMG_CFG_DELAY_4 (8b; from ISP)

AIE1ENTH = AIA_IMG_EVT_1_ENTR_TH (16b; from ISP),  	event 1 entry threshold

AIE1ENCN = AIA_IMG_EVT_1_ENTR_CNT (16b; from ISP),  	event 1 entry counts

AIE1EXTH = AIA_IMG_EVT_1_EXIT_TH (16b; from ISP),  	event 1 exit threshold

AIE1EXCN = AIA_IMG_EVT_1_EXIT_CNT (16b; from ISP),  	event 1 exit counts

AIE2ENTH = AIA_IMG_EVT_2_ENTR_TH (16b; from ISP),  	event 2 entry threshold

AIE2ENCN = AIA_IMG_EVT_2_ENTR_CNT (16b; from ISP),  	event 2 entry counts

AIE2EXTH = AIA_IMG_EVT_2_EXIT_TH (16b; from ISP),  	event 2 exit threshold

AIE2EXCN = AIA_IMG_EVT_2_EXIT_CNT (16b; from ISP),  	event 2 exit counts

AIHISMXB = AIA_IMG_HIST_MAX_BIN (16b; from ISP),    bin number of maximum of standard histogram

AIHIS192 = AIA_IMG_HISTC_BN_192 (16b; from ISP),  	cumulative histogram value at

bin #192

AIHIS348 = AIA_IMG_HISTC_BN_348 (16b; from ISP),  	cumulative histogram value at

bin #348

AIHIS604 = AIA_IMG_HISTC_BN_604 (16b; from ISP),  	cumulative histogram value at

bin #604

AIHIS860 = AIA_IMG_HISTC_BN_860 (16b; from ISP),  	cumulative histogram value at

bin #860

Quality/Sanity Check of FDB ID:  Does AIMFDBID = AFDBGID ?

3. Other Keywords

Coordinate Information (including instrument & spacecraft pointing)

CD#_#@			Dimensioned transformation matrix

CDELT#@			Pixel spacing along axis #

CROTA#			Coordinate rotation (note: PC or CD transformation matrix

is preferred)

CRPIX#@			Reference pixel along axis #

CRVAL#@			Reference value along axis #

CTYPE#@			Type of coordinate axis #

Some CTYPE axes:	   RAW	Image or array with no know coordinate mapping

SOLARX	Axis represents position East-West in arc-seconds, positive is to west from the solar disk center

SOLARY	Axis represents position North-South in arc-seconds from the solar disk center. CUNIT1 and CUNIT2 default to “arcsec” if not present.

HPLN-TAN  Helioprojective longitude, tangent projection (Same as SOLARX but CDELT1 must be in degrees).

HPLT-TAN  Helioprojective latitude, tangent projection (Same as SOLARY but CDELT2 must be in degrees).

CUNIT#@			Units along axis #

PC#_#@			Transformation matrix

R-SUN			Radius of the Sun in m (float)

DSUN_OBS			Distance from Sun’s center to SDO in m (float)

RSUN_REF			Radius of the Sun in m, depends on wavelength (float)

X0				X-axis location of solar disk center in pixels (float)

Y0				Y-axis location of solar disk center in pixels (float)

SDO_ROLL			Position angle of solar pole wrt the SDO Z axis (float, degrees)

IM_SCALE			Arc-sec per pixel default value for the particular instrument (float)

XCEN				X co-ordinate of array center (float)

YCEN				Y co-ordinate of array center (float)

where  a  = CROTA2

XCEN   = CRVAL1 + CDELT1*cos(a)*((NAXIS1+1)/2 – CRPIX1)

– CDELT2*sin(a)*((NAXIS2+1)/2 – CRPIX2)

YCEN   = CRVAL2 + CDELT1*sin(a)*((NAXIS1+1)/2 – CRPIX1)

+ CDELT2*cos(a)*((NAXIS2+1)/2 – CRPIX2)

Observation Planning Information

OBJECT			Name of object

OBJ_ID			Object identifier, e.g. active region number

OBSERVER			Name of observer

OBS_PROG			Name of the observing program

SCI_OBJ			The science objective of the observation

Temperature Information:

AIMCCTP1 = A8282 = AIA_IMG_CEB_CCD_TEMP1 (8b; from ISP)

AIMCCTP2 = A8283 = AIA_IMG_CEB_CCD_TEMP2 (8b; from ISP)

Data and Image Data Information

AIMGCPPR = A838C = AIA_IMG_COMPR_PAR (32b; from ISP)

AIMPCGT1 = A830C = AIA_IMG_PIX_COUNT_GT_TH1 (16b; from ISP)

AIMPCGT2 = A830D = AIA_IMG_PIX_COUNT_GT_TH2 (16b; from ISP)

AIMPCGT3 = A830F = AIA_IMG_PIX_COUNT_GT_TH3 (16b; from ISP)

AIMPCGT4 = A8310 = AIA_IMG_PIX_COUNT_GT_TH4 (16b; from ISP)

AIMPCLT1 = A8311 = AIA_IMG_PIX_COUNT_LT_TH1 (16b; from ISP)

AIMPCLT2 = A8312 = AIA_IMG_PIX_COUNT_LT_TH2 (16b; from ISP)

AIMPCLT3 = A8313 = AIA_IMG_PIX_COUNT_LT_TH3 (16b; from ISP)

AIMPCLT4 = A8314 = AIA_IMG_PIX_COUNT_LT_TH4 (16b; from ISP)

---------------

EXTEND			FITS file may contain extensions

COMMENT			ASCII comment (can be multiple)

HISTORY			ASCII history record (can be multiple)

FILENAME			Name of the data file

TBD: keywords for focus, GT statistics, H/K packet #, S/C info., orbit info., etc., when available and derived keywords, e.g., statistics, bad pixels, flat fielding, image center, etc.

Reformatter Information

AIVNIMST = A831A = AIA_VER_NUM_IMAGE_STATUS

ACSUM027 = APID027_CHECKSUM

VERSION

QUALITY

LEVEL NUMBER

PIPELINE VERSION

(Note: Some of the above keywords can be updated based on values in the ISP, e.g., CDELTi may be set since darks and normal images can be differentiated.

More level definitions

Definition of Level-0.3      (Note: The intended use of this level is for quick-look higher-level data products in near-real time with a few minute lag from Level-0.1.)

1.  Header

Metadata for Level-0.1 plus that generated or updated from ancillary information about instrument pointing and roll, spacecraft location and velocity using flight dynamics predict data (FDS), the time of the observation with respect to the spacecraft or instrument clock, and known errors in such clocks, as well as information concerning the state of the instrument, etc., to provide the lowest level of scientifically-useful data for quick look and other applications.

2.  Data

Decompressed raw data recompressed using gzip. (Same as that for Level-0)

(Note: Since FDS data will be available at this level, it should be possible to set CTYPEi to SOLARX and SOLARY, and add CRPIXj, CRVALi, and CROTAj estimates assuming the image is centered on the CCD.)

Definition of Level-0.5      (Note: This is a delayed but more complete version of Level-0.3, lagging real time by hours up to a day.)

1.  Header

Metadata for Level-0.3 plus that updated from the final versions of SDO HK roll information and FDS data.

2.  Data

Decompressed raw data recompressed using gzip. (Same as that for Level-0)

Definition of Level-0.8      (Note: The intended use of this intermediate, temporary data series is to facilitate quick-look observable computations lagging real time by at most a few minutes.)

1.  Header

Metadata for Level-0.3 plus updating the image coordinate mapping keywords to

meaningful and nearly correct values.

2.  Data

Decompressed raw data (level 0) calibrated by applying a flat field and then recompressed

using gzip.

(Note: At this level the following can be set: CTYPEi, CRPIXj, CRVALi, CROTAj, R_SUN, X0, Y0, XCEN, and YCEN to meaningful and nearly correct values.)

Definition of Level-0.9      (Note: This temporary level is generated on demand from Level-0.5 and is held for up to 60 days.)

1.  Header

Metadata for Level-0.5 plus the best possible flat field is applied and bad pixels are identified in a list in a second segment to be carried along with the image segment, to provide the lowest level of scientifically-useful data, with the metadata expressed in terms of the Level-1.2 AIA/SDO FITS keywords. (Note that the header and data of this level is equivalent to the lowest level provided by TRACE, except for the application of the flat field.)

2.  Data

Decompressed raw data (level 0) calibrated by applying the best possible flat field and then

recompressed using gzip.

# Text boxes

R2

R1